## Slide 1: RTL8192C USB Linux Driver Quick Installation Guide

## Slide 2: Software Package & Platform requirements
Software Package:
8192C linux driver (source code)
- support 32bits linux kernel version 2.6
8192C documents
wpa_supplicant software

## Slide 3
Software Package & Platform requirements
Platform requirements:
PC-Based Linux platform (i386)
8192C USB Linux driver supports Linux kernel version
: from 2.6.18 ~ 2.6.38

## Slide 4: HOW- TO: Setting up Linux environment
- Demonstration based on Linux Fedora 2.6.24
Part 1: make 8192C USB Linux driver
Part 2: setting up Network interface
Part 3: Site Survey & connect to AP without security

## Slide 5: Part 1: make 8192C USB Linux driver quickly
execute shell script “install.sh”
>./install.sh

## Slide 6: Part 1: make 8192C USB Linux driver step by step
(1) step1: uncompress the “rtl8192cu_linux_v3.0.xxxx.2011xxxx.tar.gz” file. (in “driver” directory)
> tar zxvf rtl8192_8188CU_linux_v3.0.2052.20110701 .tar.gz
(2) step2: make 8192C USB driver module
> make
(3) step3: clean the operation environment
> ./clean
(4) step4: insert 8192C USB modules
> insmod 8192cu.ko

## Slide 7: Part 2: setting up Network interface
(1) step1: enable wlan0 interface
  > ifconfig wlan0 up
(2) step2: setup IP address
> ifconfig wlan0 192.168.1.100

## Slide 8: Part 3: Site Survey & connect to AP without security
step1: Site Survey
> iwlist wlan0 scan
step2: Connect to AP
> iwconfig wlan0 essid “xxx”

## Slide 9
Notes: connect to AP using "Network Manager" GUI utility
  (a) Network Manager is a utility attempts to make use of wireless networking easy.
  (b) please disable the “Network Manager” when using command-line method to connect to AP, because the “Network Manager” will conflict with the method of command line.